## Slide 1: Oxygen isotope distributions of a compound CAI-chondrule object in TIL (Thiel Mountains) 07007 chondrite
N. Sakamoto1, N. Kawasaki1, C. Park2
1Hokkaido U., 2Korea Polar Research Institute
Notes: Today, I will talk about oxygen isotope distribution of a compound object using isotope mosaic map.
Today’s my talk may be more technical but I hope to introduce my way to enjoy isotope imaging.
Before we get to the topic,

## Slide 2
Notes: Please let me thank for Sapporo metsoc meeting.
This is a picture of lab tour.
Thank you very much to visit our SIMS lab and come back to Hokkaido.
For introduction, let me report the result of measurement we conducted during metsoc meeting.

## Slide 3
Isheyevo 2-3
Sakamoto and Kawasaki, 2019 metsoc
D17O ~ -37‰
10μm
Notes: During the lab tour, we had measured this section
(click)
containing one of extremely 16O-rich CAI
(click)
indicating oxygen isotopic composition of the Sun.

## Slide 4
Isheyevo 2-3
12C- 13C- 16O- 17O- 18O- 16OH- 16OD-
19F- 12C14N- 12C15N- 35Cl- 37Cl-
Notes: Yellow circles indicate measured areas for these isotopes during metsoc meeting.
Among these isotopes

## Slide 5
Isheyevo 2-3
12C- 13C- 16O- 17O- 18O- 16OH- 16OD-
19F- 12C14N- 12C15N- 35Cl- 37Cl-
Notes: I will show you the result of nitrogen.

## Slide 6: Stigmatic Isotope Imaging
Notes: This is our machine.
Cryogenic stage and SCAPS.
At first, I will explain how to get isotope image.

## Slide 7: Stigmatic Isotope Imaging
Organics
12C14N
10B16O
12C13C1H
Mass
Intensity
26.000
26.005
26.010
26.015
Notes: For nitrogen, we measure CN as nitrogen signal because of the low ionization efficiency of nitrogen single atom.
This is a mass spectrum around C12N14.
In organics case, BO is a big interference for 12C14N.

## Slide 8: Stigmatic Isotope Imaging
12C14N
10B16O
12C13C1H
Mass
Intensity
26.000
26.005
26.010
26.015
Organics
Diamond
13C13C
Notes: In diamond case, 13C13C is a main interference requiring more than 8000 mass resolving power at least.

## Slide 9: Stigmatic Isotope Imaging
12C14N
10B16O
12C13C1H
Mass
Intensity
26.000
26.005
26.010
26.015
Organics
Diamond
13C13C
Notes: If we project the mass signal on 2 dimensional ion detector,

## Slide 10: Stigmatic Isotope Imaging
Mass
Isheyevo lithic clast
12C15N
11B16O
13C14N
Exit Slit
Notes: We can see the mass image.
In the case of 12C15N on Isyeyevo lithic clast,
There is strong boron signal.
(click)
We narrow a slit to cut these interferences.

## Slide 11: Stigmatic Isotope Imaging
Mass
Isheyevo lithic clast
12C15N
11B16O
13C14N
Exit Slit
Notes: Then, we can get signal from the target isotope only.

## Slide 12: Stigmatic Isotope Imaging
Mass
Isheyevo lithic clast
12C15N
11B16O
13C14N
Exit Slit
Notes: We can use high intense beam based on the stigmatic optics for high precision and fast isotope imaging.

## Slide 13
Isheyevo 2-3
500μm
FeSO
d15N
-1000
2000
Notes: For example, this is a BSE image taken after metsoc meeting analysis.
Scale bar is 500 micron.
Circle indicates ion beam radius about 80 micrometer.
(click)
We mainly measured lithic clast at that time.
(click)
This is d15 Nitrogen mosaic map.
Color bar is -1000 to 2000.
All material in this region has higher d15N relative to earth contamination.
Several interesting stuff were found.

## Slide 14
Isheyevo 2-3
FeSO
d15N
-1000
5000
12C14N
16OH
19F
35Cl
+400 ‰
+200 ‰
d15N
Notes: This is one of them.
Nitrogen and Hydrogen, Relatively low Fluorine, high Chlorine.
(click)
This is d15N image.
This material has high and homogeneous d15N relative to surroundings.

## Slide 15
10μm
Fe
Mg
Si
S
Sakamoto@JpGU2020
Notes: This is BSE image of the material.
Scale bar is 10 micron.
This material is very weak to electron beam.
(click)
The major chemical composition is similar to surroundings.
Attached are FeS.
(click)
I will present the nitrogen study at JpGU AGU joint meeting this year.
Please come back to Japan again.

## Slide 16
TIL 07007
Notes: Let’s move on to main topic.
This is RGB map of TIL 07007 obtained by Korean Polar Research Institute.
(click)
If we look this region,

## Slide 17
CAI
AOA
CHD
CHD
CHD
AOA
CHD
AOA
CAI
AOA
CHD
CHD
CHD
CHD
CHD
CHD
CHD
CHD
AOA
CHD
CHD
CHD
CAI
CHD
MgCaAl
Notes: We can see many objects.
(click)
We normally classify to CAI, AOA or chondrule.
Most of CAIs and AOAs show O16-rich composition, chondrule show O16-poor.
Therefore, If we map an intermediate object,
(click)
We may trace the material interaction or evolution occurred in the early solar nebula using oxygen isotope.

## Slide 18
CAI
CHD
MgCaAl
Notes: This object is composed of Mg-rich region and Ca-Al-rich region.
(click)
I call this object as a compound object, and here is chondrule part and here is CAI part in this talk.

## Slide 19
MgCaAl
CAI
CHD
Notes: We mapped this compound object divided 13 by 26 areas using 80 micrometer diameter beam with 100 micrometer step.

## Slide 20
24Mg16O
LN2 depleted
Refill
Notes: This is MgO map.
Chondrule part is rich in Mg, CAI part is poor.
You may find strange area
(click) here. This is because
(click) Analysis start from here to this direction
(click) at this point, liquid nitrogen for ion imager depleted, may be I forgot, then output signal of imager increase
(click) after refill liquid nitrogen
(click) the signal become normal.

## Slide 21
16O
Notes: This is O16.
The intensity of O16 is high enough to ignore the temperature change.

## Slide 22
d18O
-80
40
16O-rich
16O-poor
d18O
Notes: This is d18O map.
Blue color indicates 16O-rich, red color indicates 16O-poor.
At first, let see........
(click)
here.

## Slide 23
Chondrule
-80
40
16O-rich
16O-poor
d18O
Notes: Here is chondrule part.
(click)
There are many 16O-rich portion.

## Slide 24
Chondrule
Relict Olivine
-80
40
16O-rich
16O-poor
d18O
Notes: When d18O and Mg image are displayed alternately
we can recognize the 16O-rich portions exist in the Mg-rich, Olivine crystals.

## Slide 25
CAI
Notes: In CAI part,

## Slide 26
CAI
Notes: Looks more blue, 16O-rich especially for this crystal and we can see Mg-poor needle like crystals.

## Slide 27
CAI
Cr
Relict Spinel
Overgrowth
D17O = -23‰
D17O = -18‰
Notes: The most 16O-rich part is spinel, outer part is slightly 16O-poor.
(click)
We also confirmed this difference by spot analysis.
(clickm repeat)
If we look at Chromium obtained by EDS, this spinel composed of Cr-poor core and Cr-rich relict.

## Slide 28
CAI
Na
Relict Anorthite
Notes: Finally, let’s see needle like crystal
(click) Anorthite.
(click, repeat)
There are 2 types of Anorthite, Na-poor and Na-rich.
(click)
Na-poor Anorthite is 16O-rich, Na-rich Anorthite is relatively 16O-poor.

## Slide 29
Notes: As we have seen, large scale isotope mosaic map
(click)
clearly help us
(click)
to understand complex history at a glance.
I stop here because of too much information.
But,

## Slide 30
TIL 07007
✓Crystal map
✓Chemical map
Isotope map
Notes: In this study, we could reveal the oxygen isotope distributions
(click) just only this region.
(click) Optical or Electron probe can give us entire crystal and chemical information.
(click)
Now, I am working on the last piece to start my meteorite study.